## Slide 1: VHDL Programming for Sequential Circuits

## Slide 2: VHDL Code for an SR Latch
library ieee;
use ieee.std_logic_1164.all;
entity srl is port(r,s:in bit; q,qbar:buffer bit);
end srl;
architecture yogesh of srl is
signal s1,r1:bit;
begin q<= s nand qbar;
qbar<= r nand q;
end yogesh;

## Slide 3: VHDL Code for a D Latch
library ieee;
use ieee.std_logic_1164.all;
entity Dl is port(d:in bit; q,qbar:buffer bit); end Dl;
architecture yogesh of Dl is signal s1,r1:bit;
begin q<= d nand qbar;
qbar<= d nand q;
end yogesh;

## Slide 4: VHDL Code for an SR Flip Flop
library ieee; use ieee.std_logic_1164.all;
entity srflip is port(r,s,clk:in bit; q,qbar:buffer bit);
end srflip;
architecture yogesh of srflip is signal s1,r1:bit;
begin s1<=s nand clk;
r1<=r nand clk; q<= s1 nand qbar;
qbar<= r1 nand q;
end yogesh;

## Slide 5: VHDL code for a JK Flip Flop
library IEEE;
use IEEE.STD_LOGIC_1164.all;
entity jk is port( j : in STD_LOGIC; k : in STD_LOGIC;
clk : in STD_LOGIC;
reset : in STD_LOGIC;
q : out STD_LOGIC; qb : out STD_LOGIC );
end jk;
architecture yyyof jk is
Begin
jkff : process (j,k,clk,reset) is
variable m : std_logic := '0';
begin
if (reset = '1')
Then
m : = '0';
elsif (rising_edge (clk)) then
if (j/ = k) then
m : = j;
elsif (j = '1' and k = '1') then
m : = not m;
end if;
end if; q <= m; qb <= not m;
end process jkff;
end yyy;

## Slide 6: VHDL Code for a D Flip Flop
Library ieee;
use ieee.std_logic_1164.all;
entity dflip is
port(d,clk:in bit; q,qbar:buffer bit);
end dflip;
architecture yyy of dflip is
signal d1,d2:bit;
begin d1<=d nand clk;
d2<=(not d) nand clk;
q<= d1 nand qbar;
qbar<= d2 nand q;
end yyy;

## Slide 7
Thank you