## Slide 1: Verilog Examples

## Slide 2: Dataflow description of a 2-to-4-line decoder
module decoder_df (A,B,E,D);
input A,B,E; output [0:3] D;
assign D[0] = ~(~A & ~B & ~E),
D[1] = ~(~A & B & ~E),
D[2] = ~(A & ~B & ~E),
D[3] = ~(A & B & ~E);
endmodu

## Slide 3: Dataflow description of a 4-bit comparator
module mag_comp (A,B,ALTB,AGTB,AEQB); input [3:0] A,B;
output ALTB,
AGTB,
AEQB; assign ALTB = (A < B),
AGTB = (A > B),
AEQB = (A == B);
endmodule

## Slide 4: Behavioral description of 2-to-1-line multiplexer
module mux2x1_bh(A,B,select,OUT);
input A,B,select;
output OUT; reg OUT;
always @ (select or A or B)
if (select == 1) OUT = A;
else OUT = B;
endmodule

## Slide 5: Description of circuit with delay
module circuit_with_delay (A,B,C,x,y);
input A,B,C;
output x,y;
wire e;
and #(30) g1(e,A,B);
or #(20) g3(x,e,y);
not #(10) g2(y,C);
endmodule

## Slide 6: D Latch
module D-latch (D, Clk, Q);
input D, Clk;
output Q;
reg Q;
always @(D or Clk)
if (Clk) Q = D;
endmodule

## Slide 7: Verilog – D Flip-flop
module D-flipflop (D, Clk, Q);
input D, Clk;
output Q;
reg Q;
always @(posedge Clk)
Q = D;
endmodule

## Slide 8
THANK YOU