## Slide 1: VHDL PROGRAM FOR LOGIC GATE

## Slide 2: Logic Operation – AND GATE
VHDL Code:
Library ieee;
use ieee.std_logic_1164.all;
entity and1 is
port(x,y:in bit ; z:out bit);
end and1;
architecture YYY of and1 is
begin z<=x and y;
end YYY;

## Slide 3: Logic Operation – OR Gate
VHDL Code:
Library ieee;
use ieee.std_logic_1164.all;
entity or1 is port
(x,y:in bit ; z:out bit);
end or1;
Architecture YYY of or1 is
begin z<=x or y;
end YYY;

## Slide 4: Logic Operation – NOT Gate
VHDL Code:
Library ieee;
use ieee.std_logic_1164.all;
entity not1 is
port(x:in bit ; y:out bit);
end not1;
architecture YYY of not1 is
begin y<=not x;
end YYY;

## Slide 5: Logic Operation – XOR Gate
VHDL Code:
Library ieee;
use ieee.std_logic_1164.all;
entity xor1 is port
(a,b:in bit ; c:out bit);
end xor1;
architecture YYY of xor1 is begin
c<=a xor b;
end YYY;

## Slide 6: Logic Operation – X-NOR Gate
VHDL Code:
Library ieee;
use ieee.std_logic_1164.all;
entity xnor1 is port
(a,b:in bit ; c:out bit);
end xnor1;
architecture YYY of xnor1 is
begin c<=not(a xor b);
end YYY;

## Slide 7
Thank you